## Slide 1
Smart City Service Robots under Extreme Climate Challenges
Team proposal -- full six-stage research methodology covering baseline ABM, concept design, A/B simulation, AI-assisted CAD optimization, ABM re-validation, and browser-deliverable digital twin. Nihonbashi, Tokyo case study.
• Cross-scale industrial-design framework combining ABM / Digital Twin and Industrial Design
• Research scenario: Nihonbashi, Tokyo -- 200 m hero scene inside 500 m station catchment
• Keywords: Extreme Climate · Aging Society · Human Heat Exposure · Urban Delivery · Emergency Services
• Authors: Sam M. Duong · Xilin Tang · Yi Tai · Qinghao · Advisor: Perry Yang
• Repository: github.com/SamDuo/nihonbashi-robot-sim
Proposal Cover
1 / 23
Based on Xilin Tang's six-stage research methodology document.

## Slide 2
Executive Summary
Run the complete six-stage methodology end to end -- from baseline ABM through high-fidelity browser-deliverable twin -- using only tools and compute the team has access to today.
• Phase 1 -- Baseline ABM of an existing Starship-type robot in the Nihonbashi scene
• Phase 2 -- Heat-Support Robot concept + variable matrix translating friction points into design
• Phase 3 -- A/B SUMO + ABM simulation with iterative feedback against the baseline
• Phase 4 -- AI + CAD optimization in Rhino / Grasshopper, Fusion 360 engineering pass
• Phase 5 -- ABM re-simulation at scale
• Phase 6 -- Browser-deliverable 3D twin + geometric sensor / motion validation
• Stretch -- NVIDIA Isaac Sim & Omniverse IF dedicated RTX hardware materializes
Summary
2 / 23
Architecture aligned to IAC-VLABB-2021 capacity + GT-licensed software stack.

## Slide 3
The Compound Problem -- Extreme Climate x Aging Society
Tokyo's compound risk -- extreme heat compounded by an aging population -- is increasing faster than passive infrastructure (cooling shelters, ambulance dispatch) can adapt.
• Heat-island effect intensified by high humidity and dense construction
• Outdoor workers and elderly residents bear disproportionate heat-exposure burden
• Fixed cooling shelters cover only fragments of Nihonbashi
• Service robots are the most direct lightweight intervention -- mobile, modular, dispatchable
• Existing designs (Starship-type) have not been tested against Nihonbashi-specific scenarios
• Without a reproducible test bed, design decisions are anecdotal -- not evidence-based
Context
3 / 23
Source: Xilin Tang slides 2-3; methodology PDF Phase One rationale.

## Slide 4
Research Questions
RQ1 -- Phases 1-3
• Can a Nihonbashi-specific service robot reduce human heat exposure during extreme heat without making sidewalks worse for pedestrians?
Build a baseline ABM of a Starship-type robot in the catchment
Identify macroscopic friction points (detours, docking, speed mismatches)
Translate frictions into the Heat-Support Robot concept & variable matrix
Run A/B simulation; iterate until Pareto-non-dominated on six metrics
RQ2 -- Phases 4-5
• Do the simulation gains hold up once the robot is designed as a real, manufacturable thing?
• Convert the variable matrix into a parametric Rhino + Fusion 360 CAD model
• Re-abstract CAD geometry into ABM parameters
• Re-run A/B at scale on the VLAB server (200+ replicates per scenario)
• Verify gains with statistical significance on >= 4 of 6 metrics
RQ3 -- Phase 6
• Can we show all of this in a browser-based 3D twin that planners and residents actually understand?
• Assemble the 500 m catchment as a 3D scene in ArcGIS Urban or CesiumJS
• Overlay heat-cost field, robot trajectories, vulnerable population, service nodes
• Validate sensor coverage + motion geometrically in Mesa with Shapely
• Demo to stakeholders; collect structured feedback
Research Questions
4 / 23
Source: team RQ framing 2026-05-19.

## Slide 5
Six-Stage Research Methodology
Phase | Name | Primary task
1 | Baseline ABM testing | Abstract a Starship-type robot into ABM; surface macroscopic friction points
2 | Product concept design | Translate friction points into Heat-Support Robot concept + variable matrix
3 | Initial A/B simulation | SUMO + ABM comparison of baseline vs. proposal; iterate the design
4 | AI + CAD optimization | Convert ABM output into manufacturable CAD model (Rhino + Fusion 360)
5 | ABM re-simulation verification | Verify macroscopic gains hold under CAD-derived parameters
6 | High-fidelity digital twin | Browser-deliverable 3D scene + geometric sensor / motion validation
Methodology
5 / 23
Source: methodology PDF Section 7; Xilin slide 8.

## Slide 6
Spatial Scope -- Nested Scales for Three Systems
Mobility, resilience, and robot service each have a natural scale. We use three nested rings so each system is observed where its dynamics actually occur.
Ring | Size | System captured | Role
Inner -- hero scene | ~200 m segment | Visualization detail | Photo-quality renders + close-ups
Middle -- service catchment | ~500 m around station | Mobility OD + resilience integral + robot routes | ABM agent simulation + Pareto comparison (Phases 1, 3, 5)
Outer -- district context | Full Nihonbashi | Policy + stakeholder framing | ArcGIS dashboard + map
• Three systems intersect at the station-catchment scale -- not the street segment
• Inner 200 m is a focal sample of the catchment, not the operational boundary
• Candidate catchments: Nihonbashi Station or Mitsukoshi-mae Station (Tokyo Metro)
• ABM compute at the catchment scale is trivially fast on the IAC-VLABB-2021 server
Spatial Scope
6 / 23
Source: team review of system-boundary question.

## Slide 7
Phase 1 -- Starship Baseline ABM Test
Abstract an existing sidewalk delivery robot into ABM-readable parameters. Drop it into the Nihonbashi catchment. Surface macroscopic friction points that motivate the design.
Starship parameters (abstracted)
• Body 569 x 697 x 616 mm
• Max speed 6 km/h (METI 2023 cap)
• Turning radius ~ 0.8 m
• Payload 10 kg, docking 30 s
• Reactive avoidance behavior
Friction points we will observe
• Pedestrian detours from docking
• Mainline / robot trajectory intersections
• Docking conflicts at service nodes
• Speed mismatches with crowd flow
• Task delays under heat conditions
• Heat-exposure overlap (shade vs. heat island)
Phase 1
7 / 23
Source: methodology PDF Phase One; Xilin slide 9.

## Slide 8
Heat-Cost Field -- GIS Bridge from Phase 1-3 Classifier into ABM
The Random Forest heat-scenario classifier from the parent Tokyo Studio repo joins the OSM sidewalk graph and becomes a scalar field consumed by every agent in the ABM.
• Per-parcel heat-scenario label (Low / Moderate / High / Extreme) from the Tokyo Studio RF classifier
• Spatial join to OSM sidewalk segments by centroid intersection
• Compute heat_cost = base_cost x (1 + heat_factor) with factor in {0.0, 0.5, 1.0, 1.5}
• Write to ABM as an edge attribute
• Pedestrian agents use heat_cost in route choice (weighted Dijkstra)
• Robot uses heat_cost for service-path optimization
• Per-agent heat_exposure accumulator integrates heat_cost x dwell_time along trajectory
• Script: scripts/build_heat_cost_field.py -- Sam owns
Phase 1 Detail
8 / 23
Source: docs/phase1_baseline.md and parent Tokyo Studio repo.

## Slide 9
Phase 2 -- Heat-Support Robot Concept Design
Transform Phase 1 friction points into a design hypothesis: a modular autonomous service robot purpose-built for extreme-heat support in dense Nihonbashi-type districts.
Body + mobility
• Body ~ 680 x 980 x 1050 mm
• Heat-resilient electronics 40 C+
• Speed throttled in dense windows
• Tighter turning radius (~ 0.6 m)
• Lift-off docking module
Service modules
• Cold water + supply delivery
• Medicine + first-aid kit drop-off
• Heatstroke response kit
• Information / wayfinding for elderly
• Modular cargo bays, swap < 60 s
Interaction cues
• Directional intent-light strip
• Top-mounted status screen
• Soft chime on docking
• Slow-for-crowd motion rhythm
• Vulnerable-pop detection mode
Phase 2
9 / 23
Source: methodology PDF Phase Two; Xilin slide 11.

## Slide 10
Phase 3 -- Initial A/B Simulation Protocol
Drop the Heat-Support Robot proposal into the same Nihonbashi scene as the Starship baseline. Same scenarios, same windows, same RNG seeds. Paired statistics.
• Scene: 500 m station catchment (with 200 m hero zone)
• Scenarios: 4 heat scenarios (cool / moderate / high / extreme) x 3 traffic windows (morning peak / midday / afternoon heat) = 12 combinations
• Replicates: 50+ paired per combination per side, with matched RNG seeds
• Side A: Starship baseline parameters Side B: Heat-Support Robot v1 parameters
• Statistical analysis: paired t-test or Wilcoxon, Holm-Bonferroni correction across six metrics
• Output: outputs/reports/phase3_comparison.md and ranked residual-issue list
Phase 3
11 / 23
Source: methodology PDF Phase Three; docs/phase3_simulation.md.

## Slide 11
Six Evaluation Metrics -- Pareto, Not Weighted Sum
Six independent metrics, scored per replicate. Pareto-non-dominated means: not worse than baseline on any metric AND strictly better on at least one. Preserves trade-offs instead of hiding them in a weighted score.
Metric | Direction | Definition
Labor Substitution Rate | Up | Fraction of outdoor delivery / patrol / resupply replaced by robots
Heat Exposure Reduction | Up | Cumulative human-staff heat exposure reduction vs. baseline
Service Continuity | Up | Service uptime during heat-scenario window
Delivery Efficiency | Up | Tasks completed per wall hour
Pedestrian Interference | Down | Detour length + speed reduction + docking conflicts
Infrastructure Compatibility | Down | Penalty for incompatible docking, charging, service-node use
Metrics
12 / 23
Source: Xilin slide 10; analysis/metrics.py.

## Slide 12
Phase 3 Iterative Feedback Loop
Phase 3 is the inner loop of the methodology. Diagnose residuals, update variables, re-run. Exit on convergence -- not on time budget.
• Run side B (proposal) against side A (baseline) with paired seeds
• Compute the six metrics for every replicate; paired-difference statistics
• Designer (Xilin) reviews ranked residual-issue list with the team
• Selectively update the proposal column of the variable matrix
• Re-run side B with new parameters; side A stays anchored to Starship
• Up to three iterations before escalating to Phase 4
• Exit criteria: (a) Pareto-non-dominated with sig on >= 4 of 6 metrics, OR (b) 3 iterations w/o significant improvement, OR (c) designer override with documented rationale
• Hand-off: final variable column + residual issues --> Phase 4
Phase 3 Loop
13 / 23
Source: methodology PDF Phase Three; docs/methodology.md exit-criteria.

## Slide 13
Phase 4 -- AI & CAD Optimization
• AI step -- summarize friction points; propose form, module placement, docking strategy, sensor placement
• Designer step (Xilin) -- select, critique, integrate against Nihonbashi & METI 2023 sidewalk-robot rules
• CAD step -- Rhino + Grasshopper primary , Fusion 360 (educational) for engineering pass
• Round-trip mapping -- every variable matrix row maps to a Rhino / Grasshopper parameter
• Output -- .3dm + .stp neutral export + .gltf for browser-side display
• Acceptance -- manufacturability review passes; every variable maps cleanly to a CAD parameter
Phase 4
14 / 23
Source: methodology PDF Phase Five.

## Slide 14
Phase 5 -- ABM Re-simulation at Scale
Re-run the A/B comparison with CAD-derived parameters. 72 logical CPUs + 768 GB RAM let us scale from 50 replicates per scenario to 200+, finishing in hours instead of days.
• Re-abstract CAD-derived geometry into ABM parameters: width, length, speed, turning radius, docking duration
• Three-tier comparison: Starship baseline (Phase 1) · Heat-Support v3 (Phase 3) · CAD-optimized (Phase 4)
• Scale up: 200+ replicates per scenario across the full 500 m catchment
• Parallelization: ~36 simultaneous Mesa workers
• Same six metrics; alpha = 0.05, power >= 0.8 thanks to the higher replicate count
• Goal: confirm Pareto-non-dominance and statistical significance hold on >= 4 of 6 metrics
• Output: outputs/reports/phase5_revalidation.md with three-way Pareto + parameter-sensitivity sweeps
Phase 5
15 / 23
Source: methodology PDF Phase Six (Part 1); IAC-VLABB-2021 compute confirmation.

## Slide 15
Phase 6.1 -- Browser-Deliverable 3D Twin
Deliver a 3D twin of the 500 m catchment that any stakeholder can open in a browser -- no client GPU, no plugin, no install. Primary: ArcGIS Experience Builder. Alternative: CesiumJS web app.
• PLATEAU LOD2 across the full catchment --> USD / glTF tiles served from the VLAB server
• Sidewalk + heat-cost field --> ArcGIS feature service / Cesium 3D Tiles overlay
• Animated robot trajectories -- played back from Phase 5 simulation traces
• Pedestrian density heatmap -- per-scenario, time-animated
• Toggleable layers: heat scenario, robot fleet, vulnerable population, service nodes, friction-point overlays
• Primary: ArcGIS Urban scene --> Experience Builder app (matches existing Tokyo Studio pipeline)
• Alternative: CesiumJS open-source twin (more programmable, browser-native)
• Trade-off: production-quality, not photoreal. LOD2 is sufficient for stakeholder map view.
Phase 6.1
16 / 23
Source: ArcGIS Urban + CesiumJS docs; matches existing Tokyo Studio publishing pipeline.

## Slide 16
Phase 6.2 -- Geometric Sensor & Motion Validation
Validate the question that actually matters -- 'do the sensors see what they need to see, and does the robot fit where it needs to fit?' -- without expensive photoreal physics. Pure geometry in Mesa.
• Robot footprint -- imported from Rhino CAD as 2D polygon with per-segment turning kinematics
• Sensor coverage as 2D polygons: camera vision cones, lidar range disc, ultrasonic ring -- Shapely
• Compute coverage % per service-node approach, blind-spot risk per docking maneuver
• Motion validation: turning radius, docking, peripheral-waiting, slope handling (proxied from elevation)
• Acceptance: trajectories within 0.5 m of CAD-specified turning radius; coverage gaps identified per service node
• What this validates: 'does the sensor placement work?' -- the load-bearing question
• What this does NOT validate: photoreal sensor fidelity, RL policies, real-hardware transfer
Phase 6.2
17 / 23
Source: Mesa + Shapely approach replacing NVIDIA Isaac Sim photoreal stack.

## Slide 17
Stretch Goal -- NVIDIA Isaac Sim Demo
IF dedicated RTX hardware materializes, we add a single 60-90 second Isaac Sim hero video. NOT load-bearing for the research conclusions. Hard constraints below.
Hard constraints (all must be true)
• Dedicated RTX 4080+ GPU -- IAC-VLABB-2021 has none
• Windows 10/11 or Ubuntu 22/24 -- NOT Server 2019
• Driver Linux 580.65+ or Windows 580.88+
• Team learning curve for Isaac Sim (unfamiliar tool)
• Robot URDF export from Rhino (Xilin time)
If unlocked -- what we deliver
• 60-90 sec hero video: robot navigating peak-commute crowd under heat
• Crude URDF (primitive boxes / cylinders) -- not photoreal CAD
• Kinematic motion validation only -- no sensor fidelity
• Visual impact for final demo; not new research evidence
• Possible hosts: GT IDEaS / PACE, NVIDIA Inception, personal RTX desktop
Stretch
18 / 23
Source: NVIDIA Isaac Sim system requirements + IAC-VLABB-2021 DxDiag.

## Slide 18
Data Inventory -- What We Have
Seven primary layers exist today. Quality stars reflect readiness across all six phases.
# | Layer | Source | Format | Quality | Owner
1 | Heat scenarios (RF classifier) | Parent Tokyo Studio repo | CSV / GeoJSON | **** | Sam, Qinghao
2 | Pedestrian GPS visits | Nihonbashi 2023 study | CSV | *** | Yi Tai
3 | OSM sidewalk graph | OSMnx | GraphML / .net.xml | **** | Yi Tai
4 | PLATEAU CityGML LOD1/LOD2 | PLATEAU VIEW 4.0 | CityGML | **** | Sam
5 | Elderly pop per parcel | e-Stat + Tokyo Metro | Shapefile | **** | Sam, Qinghao
6 | Evacuation shelters | Tokyo Open Data | CSV | **** | Sam
7 | Starship robot specs | Public spec | CSV | ** | Yi Tai
Data: Inventory
19 / 23
Source: data/README.md + parent Tokyo Studio inventory.

## Slide 19
Data Gaps -- What We Need to Acquire or Build
Critical gaps block specific phases. Should-have gaps lift fidelity but are not required.
Critical (block downstream phases)
• 1. Weather forecast (6-48 hr) for proactive dispatch -- Phase 1-3
• 2. Tokyo Fire Dept heatstroke transport data -- vulnerable-pop modeling
• 3. METI 2023 sidewalk-robot regulation -- design constraint
• 4. Pedestrian behavior under heat (GPS by temp bin) -- Phase 3
• 5. Per-segment sidewalk widths -- Phase 3, Phase 6.2
• 6. PLATEAU LOD2 catchment USD/glTF tiles -- Phase 6.1
• 7. Robot CAD source from Rhino -- Phase 5, Phase 6
• 8. Sensor specs (FOV, lidar range, ultrasonic placement) -- Phase 6.2
Should have
• 9. e-Stat 6th mesh (125 m) demographic resolution
• 10. WBGT <-> NWS Heat Index reconciliation
• 11. Vulnerable-pop dwell-time map
• 12. Nihonbashi service-node inventory (CVS, vending, toilets, transit exits)
• 13. Japanese-language signage overlay
• 14. Pre-rendered Blender hero shots for slides + video
• 15. (Stretch only) Photoreal CAD for Isaac Sim
Data: Gaps
20 / 23
Source: team M&V triage; methodology PDF Phase One data layer.

## Slide 20
Tooling Stack and Team / RACI
Every tool is free, educational, or already GT-licensed. Four contributors, async-first workflow.
Tooling by phase
• Phases 1, 3, 5 -- Python · Mesa · SUMO · GeoPandas · scikit-learn
• Phase 2 -- team review + AI assist for concept expansion
• Phase 4 -- Rhino + Grasshopper · Fusion 360 (edu) · Blender
• Phase 6.1 -- ArcGIS Urban · Experience Builder · CesiumJS
• Phase 6.2 -- Mesa + Shapely · GeoPandas
• Hosting -- Flask · Streamlit · ArcGIS Online
• Stretch -- NVIDIA Isaac Sim (conditional)
Team and RACI
• Sam (M&V lead): R/A for data, GIS, twin, server orchestration, slides
• Xilin (Design lead): R/A for Phase 2 concept, Phase 4 CAD, materials
• Yi Tai (ABM lead): R/A for Phases 1, 3, 5 simulation + metrics + Phase 6.2
• Qinghao (Domain): C for heat-risk, thermal validation, vulnerable-pop
• Advisor: I on all workstreams; sign-off on milestone reviews
Tooling + Team
22 / 23
Source: existing GT software inventory; CONTRIBUTING.md ownership map.